## Slide 1: SEQ CPU Implementation

## Slide 2: Outline
Organizing Processing into Stages
Suggested Reading 4.3.1

## Slide 3: Executing arith./log. operation
Fetch
  Read 2 bytes
Decode
  Read operand registers
Execute
  Perform operation
  Set Condition Ccodes
Memory
  Do nothing
Write back
  Update register rB
PC Update
  Increment PC by 2
OPl rA, rB
6
fn
rA
rB
opq rA, rB
6
fn
rA
rB

## Slide 4: Stage Computation: arith./log. ops
OPl rA, rB
icode:ifun  M1[PC]
rA:rB  M1[PC+1]
valP  PC+2
Fetch
Read instruction byte
Read register byte
Compute next PC
valA  R[rA]
valB  R[rB]
Decode
Read operand A
Read operand B
valE  valB ifun valA
Set CC
Execute
Perform ALU operation
Set condition code register
Memory
R[rB]  valE
Write
back
Write back result
PC  valP
PC update
Update PC
Notes: 注意：execute中的运算是valB OP valA，而不是valA OP valB
M1[PC] 表示从PC开始的内存中读取一个字节的数据。

## Slide 5: Stage Computation: arith./log. ops
valA  R[%rdx] = 9
valB  R[%rbx] = 21
OPl rA, rB
icode:ifun  M1[PC]
rA:rB  M1[PC+1]
valP  PC+2
Fetch
valA  R[rA]
valB  R[rB]
Decode
valE  valB ifun valA
Set CC
Execute
Memory
R[rB]  valE
Write
back
PC  valP
PC update
subl %rdx, %rbx 0x00c: 6123
icode:ifun  M1[0x00C] = 6:1
rA:rB  M1[0x00C+1] = 2:3
valP  0x00C+2 = 0x00E
valE  21 - 9 = 12
ZF  0, SF  0, OF  0
R[%rbx]  valE = 12
PC  valP = 0x00E
Notes: 注意：execute中的运算是valB OP valA，而不是valA OP valB
M1[PC] 表示从PC开始的内存中读取一个字节的数据。

## Slide 6
Instruction
Instruction memory
PC increment
CC
CC
ALU
Data memory
Fetch
Decode
Execute
Memory
Write back
icode:ifun, rA:rB
valC
Register
M
valP
rA, rB
rB,dstM
valA, valB
valA,valB
Cnd
valE
addrs,data
valM
PC
valE
valM
valP
PC
A B
Register File
E
M
PC
PC
CC

## Slide 7: Stage Computation: rrmovq
rrmovq rA, rB
icode:ifun  M1[PC]
rA:rB  M1[PC+1]
valP  PC+2
Fetch
Read instruction byte
Read register byte
Compute next PC
valA  R[rA]
Decode
Read operand A
valE  0 + valA
Execute
Perform ALU operation
(generalization)
Memory
R[rB]  valE
Write
back
Write back result
PC  valP
PC update
Update PC
Notes: 虽然，rrmovl在execute阶段不需要运算。但因为我们使用的是一个统一的框架，每条指令都必须通过每个阶段，所以execute总要干点什么事情。
而且，因为我们为了简化起见，在memory和write back阶段都尽量使用execute产生的结果，这样可以减少信号传递的数量。
比如，这样做以后，我们用valE作为传递给write back阶段的内容，而不是valA。这样就使得本指令的write back阶段和前面的OPq一模一样（无论是动作还是数据源）。
一个原则就是：尽可能使得每一步的操作都非常一致，这样就可以简化电路设计。
Simplicity favors regularity.

## Slide 8
Instruction
Instruction memory
PC increment
CC
CC
ALU
Data memory
Fetch
Decode
Execute
Memory
Write back
icode:ifun, rA:rB
valC
Register
M
valP
rA, srcB
rB,dstM
valA, valB
valA,0
Cnd
valE
addrs,data
valM
PC
valE,
valM
PC
A B
Register File
E
M
valP
CC
PC
PC

## Slide 9: Stage Computation: irmovq
irmovq V, rB
icode:ifun  M1[PC]
rA:rB  M1[PC+1]
valC  M8[PC+2]
valP  PC+10
Fetch
Read instruction byte
Read register byte
Read constant value
Compute next PC
Decode
valE  0 + valC
Execute
Perform ALU operation
(generalization)
Memory
R[rB]  valE
Write
back
Write back result
PC  valP
PC update
Update PC

## Slide 10
Instruction
Instruction memory
PC increment
CC
CC
ALU
Data memory
Fetch
Decode
Execute
Memory
Write back
icode:ifun, rA:rB
valC
Register
M
valP
srcA, srcB
rB,dstM
valA, valB
valC,0
Cnd
valE
addrs,data
valM
PC
valE,
valM
PC
A B
Register File
E
M
valP
CC
PC
PC

## Slide 11: Executing rmmovq
Fetch
  Read 10 bytes
Decode
  Read operand registers
Execute
  Compute effective address
Memory
  Write to memory
Write back
  Do nothing
PC Update
  Increment PC by 10
rmmovq rA, D(rB)
4
0
rA
rB
D

## Slide 12: Stage Computation: rmmovl
Use ALU for address computation
rmmovl rA, D(rB)
icode:ifun  M1[PC]
rA:rB  M1[PC+1]
valC  M8[PC+2]
valP  PC+10
Fetch
Read instruction byte
Read register byte
Read displacement D
Compute next PC
valA  R[rA]
valB  R[rB]
Decode
Read operand A
Read operand B
valE  valB + valC
Execute
Compute effective address
M8[valE]  valA
Memory
Write value to memory
Write
back
PC  valP
PC update
Update PC

## Slide 13
Instruction
Instruction memory
PC increment
CC
CC
ALU
Data memory
Fetch
Decode
Execute
Memory
Write back
icode:ifun, rA:rB
valC
Register
M
valP
rA, rB
dstE,dstM
valA, valB
valC,valB
Cnd
valE
valE,valA
valM
PC
valE,
valM
PC
A B
Register File
E
M
valP
CC
PC
PC

## Slide 14: Executing mrmovq
Fetch
  Read 10 bytes
Decode
  Read operand register rB
Execute
  Compute effective address
Memory
  Read from memory
Write back
  Update register rA
PC Update
  Increment PC by 10
mrmovq D(rB),rA
5
0
rA
rB
D
Notes: 这里有一个特点，指令中rB是在rA之前。这主要是为了和rmmovl保持统一。

## Slide 15: Stage Computation: mrmovq
Use ALU for address computation
mrmovq D(rB) , rA
icode:ifun  M1[PC]
rA:rB  M1[PC+1]
valC  M8[PC+2]
valP  PC+10
Fetch
Read instruction byte
Read register byte
Read displacement D
Compute next PC
valB  R[rB]
Decode
Read operand B
valE  valB + valC
Execute
Compute effective address
valM  M8[valE]
Memory
Read data from memory
R[rA]  valM
Write
back
Update register rA
PC  valP
PC update
Update PC
Notes: 通过让rB来寻址，就使得本指令和rmmovl在Execute阶段的运算是完全一致的。

## Slide 16
Instruction
Instruction memory
PC increment
CC
CC
ALU
Data memory
Fetch
Decode
Execute
Memory
Write back
icode:ifun, rA:rB
valC
Register
M
valP
srcA, rB
dstE,rA
valA, valB
valC,valB
Cnd
valE
valE,data
valM
PC
valE,
valM
PC
A B
Register File
E
M
valP
CC
PC
PC

## Slide 17: Executing pushq
Fetch
  Read 2 bytes
Decode
  Read stack pointer and register rA
Execute
  Decrement stack pointer by 8
Memory
  Store valA at the address of new stack pointer
Write back
  Update stack pointer
PC Update
  Increment PC by 2
pushq rA
a
0
rA
F

## Slide 18: Stage Computation: push
Use ALU to decrement stack pointer
pushq rA
icode:ifun  M1[PC]
rA:rB  M1[PC+1]
valP  PC+2
Fetch
Read instruction byte
Read register byte
Compute next PC
valA  R[rA]
valB  R[%rsp]
Decode
Read valA
Read stack pointer
valE  valB + (-8)
Execute
Decrement stack pointer
M8[valE]  valA
Memory
Store to stack
R[%rsp]  valE
Write
back
Update stack pointer
PC  valP
PC update
Update PC

## Slide 19
Instruction
Instruction memory
PC increment
CC
CC
ALU
Data memory
Fetch
Decode
Execute
Memory
Write back
icode:ifun, rA:rB
valC
Register
M
valP
rA, %rsp
%rsp,dstM
valA, valB
-8,valB
Cnd
valE
valE,valA
valM
PC
valE,
valM
PC
A B
Register File
E
M
valP
CC

## Slide 20: Executing popq
Fetch
  Read 2 bytes
Decode
  Read stack pointer
Execute
  Increment stack pointer by 8
Memory
  Read from old stack pointer
Write back
  Update stack pointer
  Update register rA
PC Update
  Increment PC by 2
popq rA
b
0
rA
F
Notes: 在写回阶段要写两个寄存器，这两个写是有先后次序的。必须按照上面的方法进行，因为rA可能就是%esp。具体见书P270 Practice Problem 4.5.

## Slide 21: Stage Computation: popq
popq rA
icode:ifun  M1[PC]
rA:rB  M1[PC+1]
valP  PC+2
Fetch
Read instruction byte
Read register byte
Compute next PC
valA  R[%rsp]
valB  R[%rsp]
Decode
Read stack pointer
Read stack pointer
valE  valB + 8
Execute
Increment stack pointer
valM  M8[valA]
Memory
Read from stack
R[%rsp]  valE
R[rA]  valM
Write
back
Update stack pointer
Write back result
PC  valP
PC update
Update PC
Use ALU to increment stack pointer
update two registers
(special: rA=%rsp)
M port takes precedenc
Notes: 比较奇特的地方是在Decode阶段，同时计算valA和valB，而这两个值是一样的，这样做显然是冗余的。
但这样做的好处是下面的整个流程就与pushl指令非常类似了。例如，在execute阶段，都是valB参与运算；
在memory阶段，都是valA参与运算。因为pop指令与pushl rmmovl mrmovl指令都是访存指令，类似之间的相似性越多，就容易实现。
在写回阶段要写两个寄存器，这两个写是有先后次序的。必须按照上面的方法进行，因为rA可能就是%esp。具体见书P270 Practice Problem 4.5.

## Slide 22
Instruction
Instruction memory
PC increment
CC
CC
ALU
Data memory
Fetch
Decode
Execute
Memory
Write back
icode:ifun, rA:rB
valC
Register
M
valP
%rsp, %rsp
%rsp,rA
valA, valB
+8,valB
Cnd
valE
valA,data
valM
PC
valE,
valM
PC
A B
Register File
E
M
valP
CC
PC
PC

## Slide 23: Executing Jumps
jXX Dest
7
fn
Dest
XX
XX
fall thru:
XX
XX
target:
Not taken
Taken

## Slide 24: Stage Computation: Jumps
jXX Dest
icode:ifun  M1[PC]
valC  M8[PC+1]
valP  PC+9
Fetch
Read instruction byte
Read destination address
Fall through address
Decode
Cnd  Cond(CC,ifun)
Execute
Take branch?
Memory
Write
back
PC  Cnd ? valC : valP
PC update
Update PC
Compute both addresses
Chose based on CC and ifun

## Slide 25
Instruction
Instruction memory
PC increment
CC
CC
ALU
Data memory
Fetch
Decode
Execute
Memory
Write back
icode:ifun, rA:rB
valC
Register
M
valP
rA, rB
rB,dstM
valA, valB
valA,valB
Cnd
valE
addrs,data
valM
PC
valE
valM
Cnd, valP, valC
PC
A B
Register File
E
M
PC
PC
CC

## Slide 26: Executing call
call Dest
8
0
Dest
XX
XX
return:
XX
XX
target:

## Slide 27: Stage Computation: call
call Dest
icode:ifun  M1[PC]
valC  M8[PC+1]
valP  PC+9
Fetch
Read instruction byte
Read destination address
Compute return point
valB  R[%rsp]
Decode
Read stack pointer
valE  valB + –8
Execute
Decrement stack pointer
M4[valE]  valP
Memory
Write return value on stack
R[%rsp]  valE
Write
back
Update stack pointer
PC  valC
PC update
Set PC to destination
Use ALU to decrement stack pointer

## Slide 28
Instruction
Instruction memory
PC increment
CC
CC
ALU
Data memory
Fetch
Decode
Execute
Memory
Write back
icode:ifun, rA:rB
valC
Register
M
valP
srcA, %rsp
%rsp,dstM
valA, valB
-8,valB
Cnd
valE
valE, valP
valM
PC
valE
valM
valC
PC
A B
Register File
E
M
PC
PC
CC

## Slide 29: Executing ret
ret
9
0
XX
XX
return:

## Slide 30: Stage Computation: ret
ret
icode:ifun  M1[PC]
Fetch
Read instruction byte
valA  R[%rsp]
valB  R[%rsp]
Decode
Read operand stack pointer
Read operand stack pointer
valE  valB + 8
Execute
Increment stack pointer
valM  M8[valA]
Memory
Read return address
R[%rsp]  valE
Write
back
Update stack pointer
PC  valM
PC update
Set PC to return address
Use ALU to increment stack pointer

## Slide 31
Instruction
Instruction memory
PC increment
CC
CC
ALU
Data memory
Fetch
Decode
Execute
Memory
Write back
icode:ifun, rA:rB
valC
Register
M
valP
%rsp, %rsp
%rsp,dstM
valA, valB
8,valB
Cnd
valE
valA,data
valM
PC
valE
valM
valM
PC
A B
Register File
E
M
PC
PC
CC

## Slide 32: Executing cmovXX
cmovXX rA, rB
2
fn
rA
rB

## Slide 33: Stage Computation: cmovXX
cmovXX rA, rB
icode:ifun  M1[PC]
rA:rB  M1[PC+1]
valP  PC+2
Fetch
Read instruction byte
Read register byte
Compute next PC
valA  R[rA]
Decode
Read operand A
valE  0 + valA
Cnd  Cond(CC,ifun)
Execute
Perform ALU operation
Take move?
Memory
Cnd ? R[rB]  valE : -
Write
back
Write back result if move taken
PC  valP
PC update
Update PC

## Slide 34
Instruction
Instruction memory
PC increment
CC
CC
ALU
Data memory
Fetch
Decode
Execute
Memory
Write back
icode:ifun, rA:rB
valC
Register
M
valP
rA, rB
rB,dstM
valA, valB
valA,0
Cnd
valE
addrs,data
valM
PC
Cnd, valE
valM
valP
PC
A B
Register File
E
M
PC
PC
CC

## Slide 35: Computation Steps
All instructions follow same general pattern
Differ in what gets computed on each step
OPq rA, rB
icode:ifun  M1[PC]
rA:rB  M1[PC+1]
valP  PC+2
Fetch
valA  R[rA]
valB  R[rB]
Decode
valE  valB OP valA
Set CC
Execute
Memory
R[rB]  valE
Write Back
PC  valP
PC update
icode,ifun
rA,rB
valC
valP
valA, srcA
valB, srcB
valE,aluA,aluB
Cond code
valM,addr,data
valE,dstE
valM,dstM
PC, newPC
call Dest
icode:ifun  M1[PC]
valC  M8[PC+1]
valP  PC+9
valB  R[%rsp]
valE  valB + –8
M8[valE]  valP
R[%rsp]  valE
PC  valC
Notes: 总结一下：最左边是各个阶段的名称，中间是各个阶段可能要用到的信号。最右边是OPl对这种一般化的实现。
对于中间一栏，dstE表示写寄存器时，从Execute阶段来的数据写到哪个寄存器；dstM表示从Memory阶段来的数据写到哪个寄存器。
只要是对于同一个东西，但数据来源不一致的就有一个相应的信号名字给它，同时用电路将各个输入加以合并。

## Slide 36
Instruction
Instruction memory
PC increment
CC
CC
ALU
Data memory
Fetch
Decode
Execute
Memory
Write back
icode:ifun, rA:rB
valC
Register
M
valP
srcA, srcB
dstE,dstM
valA, valB
aluA,aluB
Cnd
valE
addrs,data
valM
PC
valE,
valM
PC
A B
Register File
E
M
CC
newPC
PC
PC

## Slide 37: Determinate Values
Fetch
  PC Program Count
  icode Instr. Code
  ifun Instr. Function
  rA Instr. Register A
  rB Instr. Register B
  valC Instr. Constant
  valP Incremented PC
Decode
  valA Register value A
  valB Register value B
Execute
  valE ALU result
  CC Condition Code
  Cnd Condition Flag
Memory
  valM Value from Memory
Write back
  valE ALU result
  valM Value from Memory

## Slide 38: Indeterminate Values
Decode
  srcA location of valA
  rA, %rsp
  srcB location of valB
  rB, %rsp
Execute
  aluA input A of ALU
  valA, valC, +8, -8
  aluB input B of ALU
  valB, 0
Memory
  addr address of memory
  valA, valE
  data data of Memory
  valA, valP
Write back
  dstE dest. of ALU result
  rB, %rsp
  dstM dest of Memory
  rA
PC
  newPC next of PC
  valP, valC, valM
, Cnd F

## Slide 39
Instruction
Instruction memory
PC increment
CC
CC
ALU
Data memory
Fetch
Decode
Execute
Memory
Write back
icode:ifun, rA:rB
valC
Register
M
valP
srcA, srcB
dstE,dstM
valA, valB
aluA,aluB
Cnd
valE
addrs,data
valM
PC
valE,
valM
newPC
PC
A B
Register File
E
M
PC
PC
CC

## Slide 40: SEQ Summary
Sequential Processor (SEQ)
  Combinational logic + Sequential logic
  Instruction executes in sequential
  Every Instruction finished in one cycle.
  Express every instruction as series of simple steps
    Fetch, Decode, Execute, Memory, Write Back, PC

## Slide 41: SEQ Semantics
Achieve the same effect as a sequential execution of the assignment shown in the tables of Figures 4.18 to 4.21
  Though all of the state updates occur simultaneously at the clock rises to the next cycle.
  A problem: popq %rsp need to sequentially write two registers. So the register file control logic must process it.