## Slide 1: Memory Hierarchy (Ⅱ)

## Slide 2: Outline
Locality
The memory hierarchy
Cache Memory
Suggested Reading: 6.2, 6.3, 6.4

## Slide 3: Locality
Principle of Locality: Programs tend to use data and instructions with addresses near or equal to those they have used recently
  Temporal locality
    Recently referenced items are likely to be referenced again soon
  Spatial locality
    Items with nearby addresses tend to be referenced close together in time

## Slide 4: Locality
All levels of modern computer systems are designed to exploit locality
  Hardware
    Cache memory (to speed up main memory accesses)
  Operating systems
    Use main memory to speed up virtual address space accesses
    Use main memory to speed up disk file accesses
  Application programs
    Web browsers exploit temporal locality by caching recently referenced documents on a local disk

## Slide 5: Locality
int sumvec(int v[N])
{
int i, sum = 0 ;
for (i = 0 ; i < N ; i++)
sum += v[i] ;
return sum ;
}
Address | 0 | 4 | 8 | 12 | 16 | 20 | 24 | 28
Contents | v0 | v1 | v2 | v3 | v4 | v5 | v6 | v7
Access order | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8

## Slide 6: Locality
Locality in the example
  sum, i: temporal locality
  v: spatial locality
    Stride-1 reference pattern
Stride-k reference pattern
  Visiting every k-th element of a contiguous vector
  As the stride increases, the spatial locality decreases

## Slide 7: Stride-1 reference pattern
int sumarrayrows(int a[M][N]) //M=2,N=3
{
int i, j, sum = 0 ;
for (i = 0 ; i < M ; i++)
for ( j = 0 ; j < N ; j++ )
sum += a[i][j] ;
return sum ;
}
Address | 0 | 4 | 8 | 12 | 16 | 20
Contents | a00 | a01 | a02 | a10 | a11 | a12
Access order | 1 | 2 | 3 | 4 | 5 | 6

## Slide 8: Stride-N reference pattern
int sumarraycols(int a[M][N]) //M=2,N=3
{
int i, j, sum = 0 ;
for (j = 0 ; j < N ; j++)
for ( i = 0 ; i < M ; i++ )
sum += a[i][j] ;
return sum ;
}
Address | 0 | 4 | 8 | 12 | 16 | 20
Contents | a00 | a01 | a02 | a10 | a11 | a12
Access order | 1 | 3 | 5 | 2 | 4 | 6

## Slide 9: Locality
Locality of the instruction fetch
  Spatial locality
    In most cases, programs are executed in sequential order
  Temporal locality
    Instructions in loops may be executed many times

## Slide 10: Locality
Data references
  Reference array a elements in succession Spatial locality
  Reference variable sum each iteration Temporal locality
Instruction references
  Reference instructions in sequence. Spatial locality
  Cycle through loop repeatedly Temporal locality
sum = 0;
for (i = 0; i < n; i++)
sum += a[i];
return sum;

## Slide 11: Memory Hierarchy

## Slide 12: Memory Hierarchy
Fundamental properties of storage technology and computer software
  Different storage technologies have widely different access times
  Faster technologies cost more per byte than slower ones and have less capacity
  The gap between CPU and main memory speed is widening
  Well-written programs tend to exhibit good locality

## Slide 13
An example memory hierarchy

## Slide 14
Caches
Fundamental idea of a memory hierarchy:
  For each K, the faster, smaller device at level K serves as a cache for the larger, slower device at level K+1.

## Slide 15: General Cache Concepts
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
9
3
Cache
Larger, slower, cheaper memory
viewed as partitioned into “blocks”
Data is copied in block-sized transfer units
Smaller, faster, more expensive
memory caches a subset of
the blocks
4
8
8
10
14
14

## Slide 16: General Cache Concepts: Hit
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Data in block b is needed
Request: 14
14
Block b is in cache:
Hit!

## Slide 17: General Cache Concepts: Miss
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Data in block b is needed
Request: 13
Block b is not in cache:
Miss!
Block b is fetched from
memory
Request: 13
13
13
13
Block b is stored in cache
Placement policy: determines where b goes
Replacement policy: determines which block gets evicted (victim)

## Slide 18: Types of Cache Misses
Cold (compulsory) miss
  Cold misses occur because the cache is empty.
Capacity miss
  Occurs when the set of active cache blocks (working set) is larger than the cache.

## Slide 19: Types of Cache Misses
Conflict miss
  Most caches limit blocks at level k+1 to a small subset (sometimes a singleton) of the block positions at level k.
    e.g. Block i at level k+1 must be placed in block (i mod 4) at level k.
  Conflict misses occur when the level k cache is large enough, but multiple data objects all map to the same level k block.
    e.g. Referencing blocks 9, 13, 9, 13, 9, 13, ... would miss every time.

## Slide 20: General Cache Concepts: Miss
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
9
Cache
Data in block 13 is needed
Request: 13
Block 13 is not in cache:
Miss!
Block 13 is fetched from
memory
Request: 13
13
13
13
Block 13 is stored in cache

## Slide 21: Caches
Why do memory hierarchies work?
  Because of locality, programs tend to access the data at level k more often than they access the data at level k+1.
  Thus, the storage at level k+1 can be slower, and thus larger and cheaper per bit.
Big Idea: The memory hierarchy creates a large pool of storage that costs as much as the cheap storage near the bottom, but that serves data to programs at the rate of the fast storage near the top.

## Slide 22
An example memory hierarchy

## Slide 23: Examples of Caching in the Hierarchy
Hardware
0
On-Chip TLB
Address translations
TLB
Web browser
10,000,000
Local disk
Web pages
Browser cache
Web cache
Network buffer cache
Buffer cache
Virtual Memory
L3 cache
L2 cache
Registers
Cache Type
Web pages
Parts of files
Parts of files
4-KB page
64-bytes block
64-bytes block
4-8 bytes words
What is Cached?
Web proxy server
1,000,000,000
Remote server disks
OS
200
Main memory
Hardware
10
On-Chip L2
Hardware
50
On-Chip L3
AFS/NFS client
10,000,000
Local disk
Hardware + OS
200
Main memory
Compiler
0
CPU core
Managed By
Latency (cycles)
Where is it Cached?
Disk cache
Disk sectors
Disk controller
100,000
Disk firmware
L1 cache
64-bytes block
On-Chip L1
4
Hardware

## Slide 24: Cache Memory

## Slide 25: Cache Memory
History
  At very beginning, 3 levels
    Registers, main memory, disk storage
  10+ years later, 4 levels
    Register, cache, main memory, disk storage
  Modern processor, 6 levels
    Registers, SRAM L1, L2,L3 cache, main DRAM memory, disk storage
  Cache memories
    small, fast SRAM-based memories
    managed by hardware automatically

## Slide 26: Cache Memory
main
memory
I/O
bridge
bus interface
ALU
register file
CPU chip
system bus
memory bus
Cache
memory
  Hold frequently accessed blocks of main memory in caches
CPU looks first for data in L1, then in L2, then in L3, then in main memory

## Slide 27: Inserting a cache between the CPU and main memory
a b c d
block 10
p q r s
block 21
...
...
w x y z
block 30
...
The big slow main memory
has room for many 16-word
blocks.
The small fast cache has room
for two 16-word blocks.
The tiny, very fast CPU register file
has room for four 8-byte words.
The transfer unit between
the cache and main
memory is a 16-word block
(64 bytes).
The transfer unit between
the CPU register file and
the cache is a 8-byte block.
line 0
line 1

## Slide 28: Memory Accessing
For a memory accessing instruction
  movq A %rax
Access cache by A directly
If cache hit
  get the value from the cache
Otherwise,
  cache miss handling
  get the value

## Slide 29: Generic Cache Memory Organization
• • •
B–1
1
0
• • •
B–1
1
0
valid
valid
tag
tag
set 0:
B = 2b bytes
per cache block
E lines
per set
S = 2s sets
t tag bits
per line
1 valid bit
per line
• • •
• • •
B–1
1
0
• • •
B–1
1
0
valid
valid
tag
tag
set 1:
• • •
• • •
B–1
1
0
• • •
B–1
1
0
valid
valid
tag
tag
set S-1:
• • •
• • •
Cache is an array
of sets.
Each set contains
one or more lines.
Each line holds a
block of data.

## Slide 30: Cache Memory
Fundamental parameters | 
Parameters | Descriptions
S = 2s E B=2b m=log2(M) | Number of sets Number of lines per set Block size(bytes) Number of physical(main memory) address bits

## Slide 31: Cache Memory
Derived quantities | 
Parameters | Descriptions
M=2m s=log2(S) b=log2(B) t=m-(s+b) C=BES | Maximum number of unique memory address Number of set index bits Number of block offset bits Number of tag bits Cache size (bytes) not including overhead such as the valid and tag bits

## Slide 32: Addressing caches
t bits
s bits
b bits
0
m-1
<tag>
<set index>
<block offset>
Physical Address A:
0
m-1
Split into 3 parts:

## Slide 33: Direct-mapped cache
Simplest kind of cache
Characterized by exactly one line per set.
valid
valid
valid
tag
tag
tag
• • •
set 0:
set 1:
set S-1:
E=1 lines per set
cache block
cache block
cache block

## Slide 34: Accessing Direct-Mapped Caches
Three steps
  Set selection
  Line matching
  Word extraction

## Slide 35: Set selection
Use the set index bits to determine the set of interest
valid
valid
valid
tag
tag
tag
• • •
set 0:
set 1:
set S-1:
t bits
s bits
0 0 0 0 1
0
m-1
b bits
tag
set
index
block
offset
selected set
cache block
cache block
cache block

## Slide 36: Line matching
1
t bits
s bits
i
0110
0
m-1
b bits
tag
set index
block offset
selected set (i):
=1?
= ?
(1) The valid bit must be set
(2) The tag bits in the cache line must match the tag bits in the address
0110
6 7
0 1
2 3
4 5
14 15
8 9
10 11
12 13
Find a valid line in the selected set with a matching tag

## Slide 37: Word Extraction
t bits
s bits
100
i
0110
0
m-1
b bits
tag
set index
block offset
selected set (i):
block offset selects
starting byte
1
0110
6 7
0 1
2 3
4 5
14 15
8 9
10 11
12 13
W0
w7

## Slide 38: Simple Memory System Cache
Cache
  16 lines
  4-byte line size
  Direct mapped
11
10
9
8
7
6
5
4
3
2
1
0
Offset
Index
Tag

## Slide 39: Simple Memory System Cache
Idx | Tag | Valid | B0 | B1 | B2 | B3
0 | 19 | 1 | 99 | 11 | 23 | 11
1 | 15 | 0 | – | – | – | –
2 | 1B | 1 | 00 | 02 | 04 | 08
3 | 36 | 0 | – | – | – | –
4 | 32 | 1 | 43 | 6D | 8F | 09
5 | 0D | 1 | 36 | 72 | F0 | 1D
6 | 31 | 0 | – | – | – | –
7 | 16 | 1 | 11 | C2 | DF | 03

## Slide 40: Simple Memory System Cache
Idx | Tag | Valid | B0 | B1 | B2 | B3
8 | 24 | 1 | 3A | 00 | 51 | 89
9 | 2D | 0 | – | – | – | –
A | 2D | 1 | 93 | 15 | DA | 3B
B | 0B | 0 | – | – | – | –
C | 12 | 0 | – | – | – | –
D | 16 | 1 | 04 | 96 | 34 | 15
E | 13 | 1 | 83 | 77 | 1B | D3
F | 14 | 0 | – | – | – | –

## Slide 41: Address Translation Example
Address: 0x354
11
10
9
8
7
6
5
4
3
2
1
0
Offset
Index
Tag
0
0
1
0
1
0
1
0
1
1
0
0
  Offset: 0x0 Index: 0x05 Tag: 0x0D
  Hit? Yes Byte: 0x36

## Slide 42: Line Replacement on Misses
Check the cache line of the set indicated by the set index bits
  If the cache line valid, it must be evicted
Retrieve the requested block from the next level
  How to get the block ?
Current line is replaced by the newly fetched line

## Slide 43: Check the cache line
1
selected set (i):
=1?
If valid bit is set, evict the line
Tag
3
0
1
2
7
4
5
6

## Slide 44: Get the Address of the Starting Byte
Consider memory address looks like the following
Clear the last bits and get the address A
0
m-1
<tag>
<set index>
<block offset>
0
m-1
<tag>
<set index>
<block offset>
xxx… … … xxx
000 … … …000

## Slide 45: Read the Block from the Memory
Put A on the Bus (A is A’000)
A
0
A’
x
main memory
I/O
bridge
bus interface
ALU
register file
CPU chip
system bus
memory bus
Cache
memory

## Slide 46: Read the Block from the Memory
Main memory reads A’ from the memory bus, retrieves 8 bytes x, and places it on the bus
X
0
A’
x
main memory
I/O
bridge
bus interface
ALU
register file
CPU chip
system bus
memory bus
Cache
memory

## Slide 47: Read the Block from the Memory
CPU reads x from the bus and copies it into the cache line
0
A’
main memory
I/O
bridge
bus interface
ALU
register file
CPU chip
system bus
memory bus
Cache
memory
X
X

## Slide 48: Read the Block from the Memory
Increase A’ by 1, and copy Y in A’+1 into the cache line.
0
A’+1
main memory
I/O
bridge
bus interface
ALU
register file
CPU chip
system bus
memory bus
Cache
memory
XY
Y

## Slide 49: Read the Block from the Memory
Repeat several times (typically 8 )
0
A’+7
T
main memory
I/O
bridge
bus interface
ALU
register file
CPU chip
system bus
memory bus
Cache
memory
XYZUVWST

## Slide 50: Cache line, set and block
Block
  A fixed-sized packet of information
    Moves back and forth between a cache and main memory (or a lower-level cache)
Line
  A container in a cache that stores
    A block, the valid bit, the tag bits
    Other information
Set
  A collection of one or more lines

## Slide 51: Direct-mapped cache simulation
Example
M=16 byte addresses
B=2 bytes/block, S=4 sets, E=1 entry/set
Address trace (reads):
0 [0000] 1 [0001] 13 [1101] 8 [1000] 0 [0000]
x
t=1
s=2
b=1
xx
x
0
v
tag
data
0
0
0
0
1
2
3
set

## Slide 52: Direct-mapped cache simulation
Example
M=16 byte addresses
B=2 bytes/block, S=4 sets, E=1 entry/set
Address trace (reads):
0 [0000] 1 [0001] 13 [1101] 8 [1000] 0 [0000]
miss
x
t=1
s=2
b=1
xx
x
1
0
m[0]m[1]
v
tag
data
0
0
0
0 [0000] (miss)
(1)
0
1
2
3
set

## Slide 53: Direct-mapped cache simulation
Example
M=16 byte addresses
B=2 bytes/block, S=4 sets, E=1 entry/set
Address trace (reads):
0 [0000] 1 [0001] 13 [1101] 8 [1000] 0 [0000]
miss hit
x
t=1
s=2
b=1
xx
x
1
0
m[0]m[1]
v
tag
data
0
0
0
1 [0001] (hit)
(2)
0
1
2
3
set

## Slide 54: Direct-mapped cache simulation
Example
M=16 byte addresses
B=2 bytes/block, S=4 sets, E=1 entry/set
Address trace (reads):
0 [0000] 1 [0001] 13 [1101] 8 [1000] 0 [0000]
miss hit miss
x
t=1
s=2
b=1
xx
x
1
0
m[0]m[1]
v
tag
data
0
1
1
m[12]m[13]
0
13 [1101] (miss)
(3)
0
1
2
3
set

## Slide 55: Direct-mapped cache simulation
Example
M=16 byte addresses
B=2 bytes/block, S=4 sets, E=1 entry/set
Address trace (reads):
0 [0000] 1 [0001] 13 [1101] 8 [1000] 0 [0000]
miss hit miss miss
x
t=1
s=2
b=1
xx
x
1
1
m[8]m[9]
v
tag
data
0
1
1
m[12]m[13]
0
8 [1000] (miss)
(4)
0
1
2
3
set

## Slide 56: Direct-mapped cache simulation
Example
M=16 byte addresses
B=2 bytes/block, S=4 sets, E=1 entry/set
Address trace (reads):
0 [0000] 1 [0001] 13 [1101] 8 [1000] 0 [0000]
miss hit miss miss miss
x
t=1
s=2
b=1
xx
x
1
0
m[0]m[1]
v
tag
data
0
1
1
m[12]m[13]
0
0 [0000] (miss)
(5)
0
1
2
3
set

## Slide 57: Direct-mapped cache simulation
Example
M=16 byte addresses
B=2 bytes/block, S=4 sets, E=1 entry/set
Address trace (reads):
0 [0000] 1 [0001] 13 [1101] 8 [1000] 0 [0000]
miss hit miss miss miss
x
t=1
s=2
b=1
xx
x
1
0
m[0]m[1]
v
tag
data
0
1
1
m[12]m[13]
0
0 [0000] (miss)
(5)
0
1
2
3
set
Thrashing!

## Slide 58: Conflict Misses in Direct-Mapped Caches
1 float dotprod(float x[8], float y[8])
2 {
3 float sum = 0.0;
4 int i;
5
6 for (i = 0; i < 8; i++)
7 sum += x[i] * y[i];
8 return sum;
9 }

## Slide 59: Conflict Misses in Direct-Mapped Caches
Assumption for x and y
  x is loaded into the 32 bytes of contiguous memory starting at address 0
  y starts immediately after x at address 32
Assumption for the cache
  A block is 16 bytes
    big enough to hold four floats
  The cache consists of two sets
    A total cache size of 32 bytes

## Slide 60: Conflict Misses in Direct-Mapped Caches
Trashing
  Read x[0] will load x[0] ~ x[3] into the cache
  Read y[0] will overload the cache line by y[0] ~ y[3]

## Slide 61: Conflict Misses in Direct-Mapped Caches
Padding can avoid thrashing
  Claim x[12] instead of x[8]

## Slide 62: Direct-mapped cache simulation
 | Address bits |  |  | 
Address (decimal) | Tag bits (t=) | Index bits (s=2) | Offset bits (b=1) | Set number (decimal)
0 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 | 0 0 0 0 0 0 0 0 1 1 1 1 1 1 1 1 | 00 00 01 01 10 10 11 11 00 00 01 01 10 10 11 11 | 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 | 0 0 1 1 2 2 3 3 0 0 1 1 2 2 3 3

## Slide 63: Why use middle bits as index?
4-line Cache
Middle-Order
Bit Indexing
00
01
10
11
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111

## Slide 64: Direct-mapped cache simulation
 | Address bits |  |  | 
Address (decimal) | Index bits (s=2) | Tag bits (t=1) | Offset bits (b=1) | Set number (decimal)
0 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 | 00 00 00 00 01 01 01 01 10 10 10 10 11 11 11 11 | 0 0 1 1 0 0 1 1 0 0 1 1 0 0 1 1 | 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 | 0 0 0 0 1 1 1 1 2 2 2 2 3 3 3 3

## Slide 65: Why use middle bits as index?
4-line Cache
High-Order
Bit Indexing
00
01
10
11
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111

## Slide 66: Why use middle bits as index?
4-line Cache
High-Order
Bit Indexing
Middle-Order
Bit Indexing
00
01
10
11
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111

## Slide 67: Why use middle bits as index?
High-Order Bit Indexing
  Adjacent memory lines would map to same cache entry
  Poor use of spatial locality
Middle-Order Bit Indexing
  Consecutive memory lines map to different cache lines
  Can hold C-byte region of address space in cache at one time

## Slide 68: Set associative caches
Characterized by more than one line per set
valid
tag
set 0:
E=2 lines per set
set 1:
set S-1:
• • •
cache block
valid
tag
cache block
valid
tag
cache block
valid
tag
cache block
valid
tag
cache block
valid
tag
cache block

## Slide 69: Accessing set associative caches
Set selection
  identical to direct-mapped cache
valid
valid
tag
tag
set 0:
valid
valid
tag
tag
set 1:
valid
valid
tag
tag
set S-1:
• • •
t bits
s bits
0 0 0 0 1
0
m-1
b bits
tag
set index
block offset
Selected set
cache block
cache block
cache block
cache block
cache block
cache block

## Slide 70: Accessing set associative caches
Line matching and word selection
  must compare the tag in each valid line in the selected set.
(3) If (1) and (2), then
cache hit, and
block offset selects
starting byte.
1
0110
w3
w0
w1
w2
1
1001
t bits
s bits
100
i
0110
0
m-1
b bits
tag
set index
block offset
selected set (i):
=1?
= ?
(2) The tag bits in one
of the cache lines must
match the tag bits in
the address
(1) The valid bit must be set.
3
0
1
2
7
4
5
6

## Slide 71: Associative Cache
Cache
  16 lines
  4-byte line size
  2-way set associative
11
10
9
8
7
6
5
4
3
2
1
0
Offset
Index
Tag

## Slide 72: Simple Memory System Cache
Idx | Tag | Valid | B0 | B1 | B2 | B3
0 | 19 | 1 | 99 | 11 | 23 | 11
0 | 15 | 0 | – | – | – | –
1 | 1B | 1 | 00 | 02 | 04 | 08
1 | 36 | 0 | – | – | – | –
2 | 32 | 1 | 43 | 6D | 8F | 09
2 | 0D | 1 | 36 | 72 | F0 | 1D
3 | 31 | 0 | – | – | – | –
3 | 16 | 1 | 11 | C2 | DF | 03

## Slide 73: Simple Memory System Cache
Idx | Tag | Valid | B0 | B1 | B2 | B3
4 | 24 | 1 | 3A | 00 | 51 | 89
4 | 2D | 0 | – | – | – | –
5 | 2D | 1 | 93 | 15 | DA | 3B
5 | 0B | 0 | – | – | – | –
6 | 12 | 0 | – | – | – | –
6 | 16 | 1 | 04 | 96 | 34 | 15
7 | 13 | 1 | 83 | 77 | 1B | D3
7 | 14 | 0 | – | – | – | –

## Slide 74: Address Translation Example
Address: 0x354
11
10
9
8
7
6
5
4
3
2
1
0
Offset
Index
Tag
0
0
1
0
1
0
1
0
1
1
0
0
  Offset: 0x0 Index: 0x05 Tag: 0x1A
  Hit? No

## Slide 75: Set Associative Cache Simulation
Example
M=16 byte addresses
B=2 bytes/block, S=2 sets, E=2 entry/set
Address trace (reads):
0 [0000] 1 [0001] 13 [1101] 8 [1000] 0 [0000]
xx
t=2
s=1
b=1
x
x
0
v
tag
data
0
0
0
0
0
1
1
set

## Slide 76: Set Associative Cache Simulation
Example
M=16 byte addresses
B=2 bytes/block, S=2 sets, E=2 entry/set
Address trace (reads):
0 [0000] 1 [0001] 13 [1101] 8 [1000] 0 [0000]
miss
1
00
m[0]m[1]
v
tag
data
0
0
0
0 [0000] (miss)
(1)
xx
t=2
s=1
b=1
x
x

## Slide 77: Set Associative Cache Simulation
Example
M=16 byte addresses
B=2 bytes/block, S=2 sets, E=2 entry/set
Address trace (reads):
0 [0000] 1 [0001] 13 [1101] 8 [1000] 0 [0000]
miss hit
1
00
m[0]m[1]
v
tag
data
0
0
0
1 [0001] (hit)
(2)
xx
t=2
s=1
b=1
x
x
0
0
1
1
set

## Slide 78: Set Associative Cache Simulation
Example
M=16 byte addresses
B=2 bytes/block, S=2 sets, E=2 entry/set
Address trace (reads):
0 [0000] 1 [0001] 13 [1101] 8 [1000] 0 [0000]
miss hit miss
1
00
m[0]m[1]
v
tag
data
0
1
11
m[12]m[13]
0
13 [1101] (miss)
(3)
xx
t=2
s=1
b=1
x
x
0
0
1
1
set

## Slide 79: Set Associative Cache Simulation
Example
M=16 byte addresses
B=2 bytes/block, S=2 sets, E=2 entry/set
Address trace (reads):
0 [0000] 1 [0001] 13 [1101] 8 [1000] 0 [0000]
miss hit miss miss
1
00
m[0]m[1]
v
tag
data
1
11
m[12]m[13]
1
0
8 [1000] (miss)?
(4)
xx
t=2
s=1
b=1
x
x
0
0
1
1
set
LRU

## Slide 80: Line Replacement on Misses
If all the cache lines of the set are valid
  Which line is selected to be evicted ?
LFU (least-frequently-used)
  Replace the line that has been referenced the fewest times over some past time window
LRU (least-recently-used)
  Replace the line that was last accessed the furthest in the past
All of these policies require additional time and hardware

## Slide 81: Set Associative Cache Simulation
Example
M=16 byte addresses
B=2 bytes/block, S=2 sets, E=2 entry/set
Address trace (reads):
0 [0000] 1 [0001] 13 [1101] 8 [1000] 0 [0000]
miss hit miss miss
1
10
m[8]m[9]
v
tag
data
1
11
m[12]m[13]
1
0
8 [1000] (miss)
(4)
xx
t=2
s=1
b=1
x
x
0
0
1
1
set

## Slide 82: Set Associative Cache Simulation
Example
M=16 byte addresses
B=2 bytes/block, S=2 sets, E=2 entry/set
Address trace (reads):
0 [0000] 1 [0001] 13 [1101] 8 [1000] 0 [0000]
miss hit miss miss miss
1
10
m[8]m[9]
v
tag
data
1
00
m[0]m[1]
1
0
0 [0000] (miss) LRU
(5)
xx
t=2
s=1
b=1
x
x
0
0
1
1
set

## Slide 83: Fully associative caches
Characterized by all of the lines in the only one set
No set index bits in the address
set 0:
valid
valid
tag
tag
cache block
cache block
valid
tag
cache block
…
E=C/B lines in
the one and only set
t bits
b bits
tag
block offset

## Slide 84: Accessing fully associative caches
Line match and Word selection
  must compare the tag in each valid line
0
0110
w3
w0
w1
w2
1
1001
t bits
100
0110
0
m-1
b bits
tag
block offset
=1?
= ?
(3) If (1) and (2), then
cache hit, and
block offset selects
starting byte.
(2) The tag bits in one
of the cache lines must
match the tag bits in
the address
(1) The valid bit must be set.
3
0
1
2
7
4
5
6
1
0
0110
1110