## Slide 1: Memory Hierarchy (I)

## Slide 2: Outline
Random-Access Memory (RAM)
Nonvolatile Memory
Data transfer between memory and CPU
Hard Disk
Data transfer between memory and disk
SSD
Storage trends
Suggested Reading: 6.1

## Slide 3: Random-Access Memory (RAM)
Key features
  RAM is packaged as a chip.
  Basic storage unit is a cell (one bit per cell).
  Multiple RAM chips form a memory.

## Slide 4: Random-Access Memory (RAM)
Static RAM (SRAM)
  Each cell stores bit with a six-transistor circuit.
  Retains value indefinitely, if it is kept powered.
  Relatively insensitive to disturbances such as electrical noise.
Dynamic RAM (DRAM)
  Each cell stores bit with a capacitor and transistor.
  Value must be refreshed every 10-100 ms.
  Sensitive to disturbances.

## Slide 5: SRAM vs DRAM summary
Tran. Access
per bit time Persist? Sensitive? Cost Applications
SRAM 6 1X Yes No 1000x cache memories
DRAM 1 10X No Yes 1X Main memories,
frame buffers
SRAM

## Slide 6: Conventional DRAM organization
d x w DRAM:
  dw total bits organized as d supercells of size w bits
cols
rows
0
1
2
3
0
1
2
3
internal row buffer
16 x 8 DRAM chip
addr
data
supercell
(2,1)
2 bits
/
8 bits
/
memory
controller
(to CPU)
pins

## Slide 7: Reading DRAM supercell (2,1)
Step 1(a): Row access strobe (RAS) selects row 2.
Step 1(b): Row 2 copied from DRAM array to row buffer.
RAS=2
cols
rows
0
1
2
3
0
1
2
3
internal row buffer
16 x 8 DRAM chip
row 2
addr
data
2
/
8
/
memory
controller

## Slide 8: Reading DRAM supercell (2,1)
Step 2(a): Column access strobe (CAS) selects column 1.
Step 2(b): Supercell (2,1) copied from buffer to data lines, and eventually back to the CPU.
supercell
(2,1)
cols
rows
0
1
2
3
0
1
2
3
internal row buffer
16 x 8 DRAM chip
CAS=1
addr
data
2
/
8
/
memory
controller

## Slide 9: Memory modules
: supercell (i,j)
0
31
7
8
15
16
23
24
32
63
39
40
47
48
55
56
64-bit doubleword at main memory address A
addr (row = i, col = j)
data
64 MB
memory module
consisting of
eight 8Mx8 DRAMs
Memory
controller
bits
0-7
DRAM 7
DRAM 0
bits
8-15
bits
16-23
bits
24-31
bits
32-39
bits
40-47
bits
48-55
bits
56-63
64-bit doubleword to CPU chip
DIMM: dual in-line memory module
240-pin for DDR2 and DDR3
280-pin for DDR4

## Slide 10: Enhanced DRAMs
All enhanced DRAMs are built around the conventional DRAM core
Fast page mode DRAM (FPM DRAM)
  Access contents of row with [RAS, CAS, CAS, CAS, CAS] instead of [(RAS,CAS), (RAS,CAS), (RAS,CAS), (RAS,CAS)].

## Slide 11: Enhanced DRAMs
Extended data out DRAM (EDO DRAM)
  Enhanced FPM DRAM with more closely spaced CAS signals.
Synchronous DRAM (SDRAM)
  Driven with rising clock edge instead of asynchronous control signals
  Clock is electronic signals as the following
Clock

## Slide 12: Enhanced DRAMs
Double data-rate synchronous DRAM (DDR SDRAM)
  Enhancement of SDRAM that uses both clock edges as control signals.
  Different sizes of small prefetch buffers that increase the effective bandwidth
  DDR (2 bits), DDR2 (4 bits), DDR3 (8 bits), and DDR4(16bits)

## Slide 13: Enhanced DRAMs
Video RAM (VRAM)
  Like FPM DRAM, but output is produced by shifting row buffer
  Dual ported (allows concurrent reads and writes)

## Slide 14: Nonvolatile memories
DRAM and SRAM are volatile memories
  Lose information if powered off.
Nonvolatile memories retain value even if powered off
  Generic name is read-only memory (ROM).
  Misleading because some ROMs can be read and modified.

## Slide 15: Types of ROMs
Programmable ROM (PROM)
  Write once
Erasable programmable ROM (EPROM)
  Erase by ultraviolet light
  Write by a special device
  About 1000 times
Electrically erasable PROM (EEPROM)
  Reprogramming in-place on printed circuit cards
  About 100,000 times
Flash memory
  Based on EEPROM
  USB flash drive (USB 闪存盘，U盘)

## Slide 16: Nonvolatile memories
Firmware
  Program stored in a ROM
  BIOS (basic input/output system)
    Boot time code
    a small set of primitive input and output functions
  graphics cards, disk controllers
    Translate I/O (input/output) requests from the CPU

## Slide 17: Bus Structure Connecting CPU and memory
A bus is a collection of parallel wires that carry address, data, and control signals
Buses are typically shared by multiple devices

## Slide 18: Bus Structure Connecting CPU and memory
main
memory
I/O
bridge
bus interface
ALU
register file
CPU chip
system bus
memory bus
memory controller

## Slide 19: Memory read transaction
1. CPU places address A on the memory bus
ALU
register file
bus interface
A
0
A
x
main memory
I/O bridge
%rax
Load operation: movq A,%rax

## Slide 20: Memory read transaction
2. Main memory reads A from the memory bus, retrieves word x, and places it on the bus.
ALU
register file
bus interface
X
0
A
x
main memory
I/O bridge
%rax
Load operation: movq A,%rax

## Slide 21: Memory read transaction
3. CPU read word x from the bus and copies it into register %rax.
ALU
register file
bus interface
X
0
A
x
main memory
I/O bridge
%rax
Load operation: movq A,%rax

## Slide 22: Memory write transaction
ALU
register file
bus interface
A
0
A
main memory
I/O bridge
%rax
Store operation: movq %rax,A
Y
1. CPU place address A on bus. Main memory reads it and waits for the corresponding data to arrive.

## Slide 23: Memory write transaction
2. CPU places data word Y on the bus.
ALU
register file
bus interface
Y
0
A
main memory
I/O bridge
%rax
Store operation: movq %rax,A
Y

## Slide 24: Memory write transaction
3. Main memory read data word Y from the bus and stores it at address A
ALU
register file
bus interface
Y
0
A
main memory
I/O bridge
%rax
Store operation: movq %rax,A
Y

## Slide 25: What’s inside a disk drive?
Spindle
Arm
Actuator
Platters
Electronics
(including a
processor
and memory!)
SCSI
connector
Image courtesy of Seagate Technology

## Slide 26: Disk geometry
Disks consist of platters, each with two surfaces.
Each surface consists of concentric rings called tracks.
Each track consists of sectors separated by gaps.
spindle
surface
tracks
track k
sectors
gaps

## Slide 27: Disk geometry (muliple-platter view)
Aligned tracks form a cylinder.
surface 0
surface 1
surface 2
surface 3
surface 4
surface 5
cylinder k
spindle
platter 0
platter 1
platter 2

## Slide 28: Disk capacity
Capacity
  maximum number of bits that can be stored
  Vendors express capacity in units of gigabytes (GB), where 1 GB = 10^9.
Capacity is determined by these technology factors:
  Recording density (bits/in): number of bits that can be squeezed into a 1 inch segment of a track.
  Track density (tracks/in): number of tracks that can be squeezed into a 1 inch radial segment.
  Areal density (bits/in2): product of recording and track density.

## Slide 29: Disk capacity
Old fashioned disks
  Each track has the same number of sectors
Modern disks partition tracks into disjoint subsets called recording zones
  Each track in a zone has the same number of sectors, determined by the circumference of innermost track
  Each zone has a different number of sectors/track

## Slide 30: Computing disk capacity
Capacity = (# bytes/sector)
x (avg. # sectors/track)
x (# tracks/surface)
x (# surfaces/platter)
x (# platters/disk)
Example:
  512 bytes/sector
  300 sectors/track (on average)
  20,000 tracks/surface
  2 surfaces/platter
  5 platters/disk
Capacity = 512 x 300 x 20000 x 2 x 5
= 30,720,000,000
= 30.72 GB

## Slide 31: Disk operation (single-platter view)
By moving radially, the arm can position the read/write head over any track.
spindle
The disk surface
spins at a fixed
rotational rate
The read/write head
is attached to the end of the arm and flies over
the disk surface on
a thin cushion of air.

## Slide 32: Disk operation (multi-platter view)
arm
read/write heads
move in unison
from cylinder to cylinder
spindle

## Slide 33: Disk Structure - top view of single platter
Tracks divided into sectors
Surface organized into tracks
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 34: Disk Access
Head in position above a track
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 35: Disk Access
Rotation is counter-clockwise
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 36: Disk Access – Read
About to read blue sector
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 37: Disk Access – Read
After BLUE read
After reading blue sector
Read one sector each time!
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 38: Disk Access – Read
After BLUE read
Red request scheduled next
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 39: Disk Access – Seek
After BLUE read
Seek for RED
Seek to red’s track
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 40: Disk Access – Rotational Latency
After BLUE read
Seek for RED
Rotational latency
Wait for red sector to rotate around
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 41: Disk Access – Read
After BLUE read
Seek for RED
Rotational latency
After RED read
Complete read of red
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 42: Disk Access – Service Time Components
Try to read RED
Seek for RED
Rotational latency
After RED read
Seek
Rotational
latency
Data transfer
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 43: Disk access time
Average time to access some target sector approximated by
  Taccess = Tavg seek + Tavg rotation + Tavg transfer
Seek time
  Time to position heads over cylinder containing target sector.
  Typical Tavg seek = 9 ms

## Slide 44: Disk access time
Rotational latency
  Time waiting for first bit of target sector to pass under r/w head.
  Tavg rotation = 1/2 x 1/RPMs x 60 sec/1 min
Transfer time
  Time to read the bits in the target sector.
  Tavg transfer = 1/(avg # sectors/track) x 1/RPM x 60 secs/1 min.

## Slide 45: Disk access time example
Example:
  Rotational rate 7,200 RPM
  Tavg seek 9 ms
  Avg # sectors/track 400
  Tavg rotation = 1/2 * (60secs/7200RPM) * 1000ms/sec
  = 4ms
  Tavg transfer = 1/400secs/track x 60sec/7200RPM * 1000ms/sec
  = 0.02 ms
  Taccess = 9 ms + 4 ms + 0.02 ms

## Slide 46: Disk access time example
Important points
  Access time dominated by seek time and rotational latency, about 10ms for 512 bytes
  First bit in a sector is the most expensive, the rest are free
  SRAM access time is about 4 ns/64-bit word
  DRAM is about 60 ns/64-bit word
  Disk is about 40,000 times slower than SRAM
  Disk is about 2,500 times slower then DRAM

## Slide 47: Logical disk blocks
Modern disks present a simpler abstract view of the complex sector geometry:
  The set of available sectors is modeled as a sequence of B sector-size logical blocks (0, 1, ...,B-1)
Mapping between logical blocks and actual (physical) sectors
  Maintained by hardware/firmware device called disk controller
  Converts requests for logical blocks into (surface, track, sector) triples.

## Slide 48: Formatted disk capacity
Allows controller to set aside spare cylinders for each zone
  Accounts for the difference in “formatted capacity” and “maximum capacity”

## Slide 49
main
memory
I/O
bridge
bus interface
ALU
register file
CPU chip
system bus
memory bus
disk
controller
graphics
adapter
USB
controller
mouse
keyboard
monitor
disk
I/O bus
Expansion slots for
other devices such
as network adapters
Host Bus
Adaptor
SCSI/SATA
Peripheral Component Interconnect
(PCI)
solid stat disk
Disk drive

## Slide 50: Memory-mapped I/O
There are processors in controllers and adapters
I/O Port
  A reserved address in the address space
  Some registers in the above processors are mapped to these addresses
Each device is associated with
  One or more ports when it is attached to the bus
the CPU can communicate with an I/O device via its I/O ports

## Slide 51: Reading a disk block
main
memory
ALU
register file
CPU chip
disk
controller
graphics
adapter
USB
controller
mouse
keyboard
monitor
disk
I/O bus
bus interface
1. CPU initiates a disk read by writing a command, logical block number, and destination memory address to ports (addresses) associated with the disk controller

## Slide 52: Reading a disk sector
main
memory
ALU
register file
CPU chip
disk
controller
graphics
adapter
USB
controller
mouse
keyboard
monitor
disk
I/O bus
bus interface
2. Disk controller translates the block to (surface, track, sector), then reads the sector and performs a DMA (direct memory access) transfer into main memory

## Slide 53: DMA
Direct memory access
A device performs a read or write bus transaction on its own, without any involvement of the CPU
The transfer of data is known as a DMA transfer

## Slide 54: Reading a disk block
main
memory
ALU
register file
CPU chip
disk
controller
graphics
adapter
USB
controller
mouse
keyboard
monitor
disk
I/O bus
bus interface
3. When the DMA transfer completes, the disk controller notifies the CPU with an interrupt (i.e., asserts a special “interrupt” pin on the CPU)
Interrupt

## Slide 55: Interrupt
I/O devices trigger interrupts by signaling a pin on the processor chip
  network adapters, disk controllers, timer chips
I/O devices place a number onto the system bus
  identifies the device that caused the interrupt
Cause the CPU stop what it is currently working on, and jump to an operating system routine

## Slide 56: Solid State Disk (SSD)
Solid state disk (SSD) is a storage technology, based on flash memory
  SSD package plugs into a standard disk slot on the I/O bus (typically USB or SATA)
  Flash translation layer = disk controller

## Slide 57: Solid State Disk (SSD)
Pages: 512B to 4KB, Blocks: 32 to 128 pages
Data read/written in units of pages.
Page can be written only after its block has been erased
A block wears out after 100,000 repeated writes.
Flash
translation layer
I/O bus
Page 0
Page 1
Page P-1
…
Block 0
…
Page 0
Page 1
Page P-1
…
Block B-1
Flash memory
Solid State Disk (SSD)
Requests to read and write logical disk blocks
different

## Slide 58: SSD Performance Characteristics
Why are random writes slow?
  Erasing a block is slow (around 1 ms)
  modify a page triggers a copy of all useful pages in the block
    Find an used block (new block) and erase it
    Copy other pages from old block to the new block
    write the page
Sequential read tput 550 MB/s Sequential write tput 470 MB/s
Random read tput 365 MB/s Random write tput 303 MB/s
Avg.seq read access 50 us Avg. seq write access 60 us

## Slide 59: SSD Tradeoffs vs Rotating Disks
Advantages
  No moving parts  faster, less power, more rugged
Disadvantages
  Have the potential to wear out
    Mitigated by “wear leveling logic” in flash translation layer
    e.g. Intel X25 guarantees 1 petabyte (1015 bytes) of random writes before they wear out
  About 30 times more expensive per byte
Applications
  MP3 players, smart phones, laptops
  Now also in desktops and servers

## Slide 60: Storage Trends
Metric 1985 1990 1995 2000 2005 2010 2015 2015:1985
$/MB 880 100 30 1 0.1 0.06 0.02 44,000
access (ns) 200 100 70 60 50 40 20 10
typical size (MB) 0.256 4 16 64 2,000 8,000 16,000 62,500
DRAM
SRAM
Metric 1985 1990 1995 2000 2005 2010 2015 2015:1985
$/GB 100,000 8,000 300 10 5 0.3 0.03 3,333,333
access (ms) 75 28 10 8 4 3 3 25
typical size (GB) 0.01 0.16 1 20 160 1,500 3000 1,500,000
Disk
Metric 1985 1990 1995 2000 2005 2010 2015 2015:1985
$/MB 2,900 320 256 100 75 60 25 116
access (ns) 150 35 15 3 2 1.5 1.3 115

## Slide 61: CPU Clock Rates
 | 1985 | 1990 | 1995 | 2000 | 2003 | 2005 | 2010 | 2015 | 2015:1985
CPU | 80286 | 80386 | Pent. | P-III | Pent.4 | Core 2 | Core i7(n) | Core i7(h) | ---
Clock rate (MHz) | 6 | 20 | 150 | 600 | 3,300 | 2,000 | 2,500 | 3,000 | 500
Cycle time (ns) | 166 | 50 | 6 | 1.6 | 0.3 | 0.5 | 0.4 | 0.33 | 500
Cores | 1 | 1 | 1 | 1 | 1 | 2 | 4 | 4 | 4
Effective cycle time (ns) | 166 | 50 | 6 | 1.6 | 0.3 | 0.25 | 0.10 | 0.08 | 2,075
Inflection point in computer history
when designers hit the “Power Wall”

## Slide 62: The CPU-Memory Gap
The gap widens between DRAM, disk, and CPU speeds.
Disk
DRAM
CPU
SSD

## Slide 63: The CPU-Memory Gap
The gap widens between DRAM, disk, and CPU speeds.
Disk
DRAM
CPU
SSD
The key to bridging this CPU-Memory gap is a fundamental property of computer programs known as locality