## Slide 1: Introducing to Y86

## Slide 2: Topics
Y86 instruction set architecture
Why do we need to study CPU design
RISC vs. CISC
Suggested Reading: 4.1

## Slide 3: Goal
Understanding the instruction encodings
Preparing for designing your
  assembler
  simulator
  computer

## Slide 4: Y86 Processor State
Program Registers
  Same 15 as with IA64. Each 64 bits
Program Counter
  Indicates address of instruction
PC
%rax
%rcx
%rdx
%rbx
%rsi
%rdi
%rsp
%rbp
Program registers
%r8
%r9
%r10
%r11
%r12
%r13
%r14

## Slide 5: Y86 Processor State
Condition Codes
  Single-bit flags set by arithmetic or logical instructions
    OF: Overflow ZF: Zero SF: Negative
Status code
  Program is running normally
  Or some special event has occured
Memory
  Byte-addressable storage array
  Words stored in little-endian byte order
Condition codes
Memory
OF
ZF
SF
Program status

## Slide 6: Y86 Instructions
Format
  1--10 bytes of information read from memory
    Can determine instruction length from first byte
    Not as many instruction types, and simpler encoding than with IA64
  Each accesses and modifies some part(s) of the program state

## Slide 7: Y86 Instructions

## Slide 8: Encoding Registers
Each register has 4-bit ID
  Same encoding as in IA64, except %r15
Register ID F indicates “no register”
  Will use this in our hardware design in multiple places
%rax
%rcx
%rdx
%rbx
%rsi
%rdi
%rsp
%rbp
0
1
2
3
6
7
4
5
1
%r8
%r9
%r10
%r11
%r12
%r13
%r14
None
8
9
A
B
C
D
E
F

## Slide 9: Instruction Example
Addition Instruction
  Add value in register rA to that in register rB
    Store result in register rB
    Note that Y86 only allows addition to be applied to register data
  Set condition codes based on result
addq rA, rB
0
6
rA
rB
Encoded Representation
Generic Form

## Slide 10: Instruction Example
Addition Instruction
  e.g., addq %rax,%rsi Encoding: 60 06
  Two-byte encoding
    First indicates instruction type
    Second gives source and destination registers
addq rA, rB
0
6
rA
rB
Encoded Representation
Generic Form

## Slide 11: Arithmetic and Logical Operations
  Refer to generically as “OPl”
  Encodings differ only by “function code”
    Low-order 4 bites in first instruction word
  Set condition codes as side effect
  Notice: no multiply or divide operation
addq rA, rB
6
0
rA
rB
subq rA, rB
6
1
rA
rB
andq rA, rB
6
2
rA
rB
xorq rA, rB
6
3
rA
rB
Add
Subtract (rA from rB)
And
Exclusive-Or
Instruction Code
Function Code

## Slide 12: Move Operations
Like the IA64 movl instruction
Simpler format for memory addresses
Give different names to keep them distinct
rrmovq rA, rB
2
0
rA
rB
Register --> Register
Immediate --> Register
irmovq V, rB
3
0
F
rB
V
Register --> Memory
rmmovq rA, D(rB)
4
0
rA
rB
D
Memory --> Register
mrmovq D(rB), rA
5
0
rA
rB
D

## Slide 13: Move Instruction Examples
IA64
Y86
—
movq $0xabcd, (%rax)
—
movl %rax, 12(%rax,%rdx)
—
movl (%rbp,%rax,8),%rcx
irmovq $0xabcd, %rdx
movq $0xabcd, %rdx
rrmovq %rsp, %rbx
movq %rsp, %rbx
mrmovq -12(%rbp),%rcx
movq -12(%rbp),%rcx
rmmovq %rsp,0x12345c(%rdx)
movq %rsp,0x12345(%rdx)

## Slide 14: Move Instruction Examples
Y86
Encoding
irmovq $0xabcd, %rdx
30 F2 cd ab 00 00 00 00 00 00
rrmovq %rsp, %rbx
20 43
mrmovq -12(%rbp),%rcx
50 15 f4 ff ff ff ff ff ff ff
rmmovq %rsp,0x12345(%rdx)
40 42 45 23 01 00 00 00 00 00

## Slide 15: Conditional Move Operations
cmovle rA, rB
2
1
rA
rB
cmovl rA, rB
2
2
rA
rB
cmove rA, rB
2
3
rA
rB
cmovne rA, rB
2
4
rA
rB
cmovge rA, rB
2
5
rA
rB
cmovg rA, rB
2
6
rA
rB
Refer to generically as “cmovXX”
  Share the same “instruction code” with rrmovl
Encodings differ only by “function code”
Based on values of condition codes
Same as IA64 counterparts

## Slide 16: Jump Instructions
  Refer to generically as “jXX”
  Encodings differ only by “function code”
  Based on values of condition codes
  Same as IA64 counterparts
  Encode full destination address
    Unlike PC-relative addressing seen in IA64
jmp Dest
7
0
Jump Unconditionally
Dest
jle Dest
7
1
Jump When Less or Equal
Dest
jl Dest
7
2
Jump When Less
Dest
je Dest
7
3
Jump When Equal
Dest
jne Dest
7
4
Jump When Not Equal
Dest
jge Dest
7
5
Jump When Greater or Equal
Dest
jg Dest
7
6
Jump When Greater
Dest

## Slide 17: Y86 Program Stack
Region of memory holding program data
Used in Y86 (and IA64) for supporting procedure calls
Stack top indicated by %rsp
  Address of top stack element
Stack grows toward lower addresses
  Top element is at lowest address in the stack
%rsp
Increasing
Addresses
Stack Top
Stack Bottom
•
•
•

## Slide 18: Stack Operations
Decrement %rsp by 8
Store word from rA to memory at %rsp
Like IA64 (pushq %rsp  save old %rsp)
Read word from memory at %rsp
Save in rA
Increment %rsp by 8
Like IA64 (popq %rsp  movq (%rsp) %rsp)
pushq rA
a
0
rA
F
popq rA
b
0
rA
F

## Slide 19: Subroutine Call and Return
Push address of next instruction onto stack
Start executing instructions at Dest
Like IA64
Pop value from stack
Use as address for next instruction
Like IA64
call Dest
8
0
Dest
ret
9
0

## Slide 20: Miscellaneous Instructions
Don’t do anything
Stop executing instructions
IA64 has comparable instruction, but can’t execute it in user mode
We will use it to stop the simulator
nop
1
0
halt
0
0

## Slide 21: Y86 Instructions

## Slide 22: Y86 Programs
int Sum(int *Start, int Count)
{
int sum = 0;
while (Count) {
sum += *Start;
Start++;
Count--;
}
return sum;
}

## Slide 23: Y86 Assembly
IA64 code
1 sum:
2 movl $0, %eax
3 jmp .L2
4 .L3:
5 addq (%rdi), %rax
6 addq $8, %rdi
7 subq $1, %rsi
8 .L2:
9 testq %rsi, %rsi
10 jne .L3
11 rep; ret
Y86 code
int Sum(int *Start, int Count)
1 sum:
2 irmovq $8,%r8
3 irmovq $1,%r9
4 xorq %rax,%rax
5 andq %rsi,%rsi
6 jmp test
7 loop:
8 mrmovq (%rdi),%r10
9 addq %r10,%rax
10 addq %r8,%rdi
11 subq %r9,%rsi
12 test:
13 jne loop
14 ret

## Slide 24: Y86 Object Program
1 # Execution begins at address 0
2 .pos 0
3 irmovq stack, %rsp # Set up stack pointer
4 call main # Execute main program
5 halt # Terminate program
6
Init part of program generated automatically
Assembler directives
  .pos 0, .pos 0x200
  .align
Symbolic Name

## Slide 25: Y86 Object Program
7 # Array of 4 elements
8 .align 8
9 array:
10 .quad 0x000d000d000d
11 .quad 0x00c000c000c0
12 .quad 0x0b000b000b00
13 .quad 0xa000a000a000
14
Data area
  array denotes the start of an array
  Aligned on 8-byte boundary

## Slide 26: Y86 Object Program
15 main:
16 irmovq array,%rdi
17 irmovq $4,%rsi
18 call sum # sum(array, 4)
19 ret
20

## Slide 27: Y86 Object Program
21 # long sum(long *start, long count)
22 # start in %rdi, count in %rsi
23 sum:
24 irmovq $8,%r8 # Constant 8
25 irmovq $1,%r9 # Constant 1
26 xorq %rax,%rax # sum = 0
27 andq %rsi,%rsi # Set CC
28 jmp test # Goto test

## Slide 28: Y86 Object Program
29 loop:
30 mrmovq (%rdi),%r10 # Get *start
31 addq %r10,%rax # Add to sum
32 addq %r8,%rdi # start++
33 subq %r9,%rsi # count--. Set CC
34 test:
35 jne loop # Stop when 0
36 ret # Return
37
38 # Stack starts here and grows to lower addresses
39 .pos 0x200
40 stack:

## Slide 29: Y86 Object Program
38 # Stack starts here and grows to lower addresses
39 .pos 0x200
40 stack:
Programmers must write assembly codes themselves
  including manage the memory
    such as allocate memory for array and stack
    as well as avoid the memory overwritting
Symbolic Name

## Slide 30: Assembling Y86 Program
Generates “object code” file eg.yo
  Actually looks like disassembler output
  unix> yas eg.ys

## Slide 33: Simulating Y86 Program
Instruction set simulator
  Computes effect of each instruction on processor state
  Prints changes in state from original
  unix> yis eg.yo

## Slide 34: Simulating Y86 Program

## Slide 35: Why do We Study the CPU Design?
Understand basic computer organization
  Instruction set architecture
Deeply explore the CPU working mechanism
  How the instruction is executed
Help you programming
  Fully understand how computer is organized and works will help you write more stable and efficient code

## Slide 36: Instruction Set Architecture #1
What is ISA ?
  Assemble Language Abstraction
    assembly supported by a processor
  Machine Language Abstraction
    Byte-level representation
What does it provide?
  An abstraction of the real computer, hide the details of implementation
    The syntax of computer instructions
    The semantics of instructions
    The execution model
    Programmer-visible computer status

## Slide 37: Instruction Set Architecture #2
Assembly Language View
  Processor state
    Registers, memory, …
  Instructions
    addq, movq, leaq, …
    How instructions are encoded as bytes
Layer of Abstraction
  Above: how to program machine
    Processor executes instructions in a sequence
  Below: what needs to be built
    Use tricks to make it run fast
    E.g., execute multiple instructions simultaneously
Compiler
OS
CPU
Design
Circuit
Design
Chip
Layout
Application
Program
ISA

## Slide 38: Instruction Set Architecture #3
ISA define the processor family
  Two main kind: RISC and CISC
    RISC: SPARC, MIPS, PowerPC, ARM
    CISC: X86 (or called IA32)
Under same ISA, there are many different processors
  From different manufacturers
    X86 from Intel, AMD and VIA
  Different models
    8086, 80386, Pentium, atom, core i7
Notes: This is the modern division. There are other kinds besides superscalar, VLIW and EPIC, e.g. vector machine, stack machine (example is X87)
We will cover some of these topics in the last lesson of cpu design.

## Slide 39: RISC vs. CISC
ISA
  Instruction set architecture
    Instructions supported by a particular processor
    Their byte-level encodings
CISC
  Complex instruction set computer
RISC
  Reduced instruction set computer

## Slide 40: CISC
Involved from the earliest computers
Mainframe and Minicomputers
  By the early 1980s
  their instruction sets had grown quite large
    Manipulating circular buffers
    performing decimal arithmetic
    evaluating polynomials
Microcomputer
  Appeared in 1970s, had limited instruction sets
    constrained by number of transistors on a single chip
  By the early 1980s, followed the path to increase their instruction sets

## Slide 41: RISC
Developed in the early 1980s
  philosophy
    One are able to generate efficient code for a simpler form of instruction set
    Complex instructions are hard to generated with a compiler and seldom used
John Cocke (1925-2002)
  1987 ACM Turing Award
David Patterson(UC Berkeley), John Hennessy (Stanford U)
  2017 ACM Turing Award

## Slide 42: RISC
IBM | Power
IBM and Motorola | PowerPC
Sun Microsystems | SPARC
Digital Equipment Corporation | Alpha
Hewlett Pack | Pa-risc
MIPS Technologies | MIPS
Acorn Computers Ltd | ARM(Acorn RISC Machine)

## Slide 43: RISC vs. CISC
CICS | Early RISC
A large number of instructions | Many fewer instructions (<100)
Some instructions with long execution times | No instruction with a long execution time
Variable-length encodings. (x86-64 1~15 bytes) | Fixed-length encodings
Multiple formats for specifying operands | Simple addressing formats
Arithmetic and logical operations can be applied to both memory and register operands | Arithmetic and logical operations only use register operands. load/store Architecture

## Slide 44: RISC vs. CISC
CICS | Early RISC
Implementation artifacts hidden from machine level programs | Implementation artifacts exposed to machine level programs
Condition codes | explicit test instructions store the test results in normal registers for use in conditional evaluation
Stack-intensive procedure linkage | Registers are used for procedure arguments and return addresses

## Slide 45: RISC
Cons for early RISC
  More instructions
  Not multiple cycles
  Exposing implementation artifacts to machine level programs
Pros for RISC
  Well suited for pipeline (high efficient implementation)

## Slide 46: Y86-64
The Y86-64 instruction set
  Includes attributes of both CISC and RISC
  Can be viewed as taking a CISC instruction set (x86-64) and simplifying it by applying some of the principles of RISC
On the CISC side
  condition codes, variable-length instructions
  uses the stack to store return addresses.
On the RISC side,
  a load/store architecture
  a regular instruction encoding
  passes procedure arguments through registers

## Slide 47: RISC vs. CISC
In the early 1990s, the debate diminished
  neither RISC nor CISC in their purest forms are better than designs that incorporated the best ideas of both

## Slide 48: RISC
Evolved and introduced more instructions
  many of which take multiple cycles to execute
  Have hundreds of instructions
Exposing implementation artifacts to machine-level programs
  proved to be shortsighted
  As new processor models were developed
    using more advanced hardware structures,
    many of these artifacts became irrelevant,
    but they still remained part of the instruction set

## Slide 49: CISC
The core of RISC design
  is well suited to execution on a pipelined machine
X86 incorporates RISC features
  Dynamic translating CISC instructions to RISC-like ops and taking pipeline architectures
  X86-64 introduces more RISC features

## Slide 50: CISC
Marketing issues determine the success of the ISAs
  X86 wins in high-end server, desktop, laptop machines
  RISC win in market of embedded processors and the smart phone

## Slide 51: CISC
Intel made it easy to keep moving from one generation of processor to the next
  By maintaining compatibility with its existing processors
As integrated-circuit technology improved
  x86 processor manufacturers could overcome the inefficiencies created by the original 8086 instruction set design
  using RISC techniques to produce performance comparable to the best RISC machines.

## Slide 52: CISC
RISC processors have done very well in the market for embedded processors
In these applications, saving on cost and power is more important than maintaining backward compatibility
  In terms of the number of processors sold
this is a very large and growing market